## Slide 1: Volume 1_Section 1 Chapter 12: Healthcare Waste Management

## Slide 2: Chapter Outline
Overview
Risks related to heath care waste
Categories of heath care waste
Sources of health care waste
Management of heath care waste
Summery

## Slide 3: Chapter Objectives
Define Health care waste
Describe risks related to health care waste
Framework of types of health care waste
Understand the stapes in Health care waste management
Demonstrate how health care waste are collected, transported, stored, treated and disposed in a heath care facility
Describe the method of health care waste disposal

## Slide 4: Overview
Health-care waste is a by-product of health care that includes potential risk and non-risk wastes. It includes all the waste generated by healthcare establishments, research facilities and laboratories.
A health care facility is responsible for managing public health and protecting the environment with regard to the waste produced.
However, the waste management process (generation, collection, transport, storage, and disposal) entails considerable complexity, involving clinical and non-clinical staff across a facility, and often depends on outside agencies.

## Slide 5: Risks Related to Healthcare Waste
Exposure to
  Pathogenic organisms,
  Harmful chemicals,
  Toxins, or
  Radioactive substances, and
Injury from sharp items.
Exposure to toxic agents
Potential cause for Infection

## Slide 6: Categories of Healthcare Wastes
  Non – Hazardous HCW
  Hazardous HCW
Approximately 75–90% of the general waste produced by health care facilities is non-contaminated.
And poses no risk of infection for those who handle it. Similar in nature to municipal waste, all or most general waste can be discarded in dumps or landfills or burned in incinerators. (WHO 2014).

## Slide 7: Categories of Waste Generated by Health Care Facilities
Sharps waste
Infectious waste
Pathological waste
Pharmaceutical waste
Cytotoxic waste
Chemical waste
Radioactive waste

## Slide 8: Management of Health Care Waste
  Reduction of Healthcare Waste
  The preferred strategies for reducing health care waste are to
    Minimize waste generation by preventing waste production,
    Reducing waste production,
    Reusing and recycling waste, and
    Recovering useful substances from waste.
  The least preferable strategy is treating and disposing of health care waste.

## Slide 9: Segregation of Waste at Point of Generation
Type of Waste | Color of Container and Markings | Type of Container
Highly infectious waste (includes all pathological waste) | Yellow, marked “highly infectious” with biohazard symbol | Strong, leak-proof plastic bag or container capable of being autoclaved
Other infectious waste | Yellow with biohazard symbol | Leak-proof plastic bag or container
Sharps | Yellow, marked “SHARPS” with biohazard symbol | Puncture-proof container
Chemical and pharmaceutical waste | Brown, labeled with appropriate hazard symbol | Plastic bag or rigid container
Radioactive waste | Labeled with radiation symbol | Lead box
General health care waste | Black | Plastic bag or container

## Slide 10: Collection and Transportation of Waste in Health Care Facilities
Waste collection timetables for each route should be carefully planned according to the waste generation patterns of the various departments.
Collect waste on a regular basis such as daily or sooner if needed according to the rate it is generated and the size of the waste containers.
Do not mix infectious/hazardous and general waste during collection or transport.
Collect and transport infectious waste to disposal sites in leak-proof, covered, contaminated-waste containers.
Do not use equipment (e.g., wheelbarrow, trolley/cart) that is used to hold and transport wastes for any other purpose in the health care facility.
Use PPE when handling wastes.

## Slide 11: Steps for collection and transport of solid infectious wastes:
Step 1
Wear full PPE when handling and transporting all waste.
Step 2
Collect waste containers and transport to the storage area or treatment area for final disposal.
Step 3
Clean and disinfect infectious-waste containers each time they are emptied
Step 4
Step 5
Remove utility gloves and perform hand hygiene after handling wastes
Wash and dry gloves

## Slide 12: Storage of Waste in Health Care Facilities
An easy-to-clean, hard floor with good drainage
Separate areas for infectious and general waste
Separate cabinets to store pharmaceutical and other toxic wastes
A good water supply with a sink for hand hygiene
Regular cleaning
Identification (signs) as a “waste storage area”
Lockable door/gate.

## Slide 13: Disposal of Health Care Waste
Choosing the best currently available waste disposal method
Working towards safer waste disposal to protect the community and the environment is essential.

## Slide 14: Disposal of Healthcare Waste Cont’d…
Healthcare Waste
Hazardous
Non Hazardous
Biodegradable (Kitchen, Landscape)
To Compost
Inorganic
Recyclable
To Market
Other

## Slide 15: Disposal of Healthcare Waste Cont’d…
Hazardous
Hazardous Cytotoxic drug, toxic chemicals, radioactive waste stored in cement tanks until half life
Sharps
Clinical Waste (Infectious Waste)
Non-Sharp
Steam Sterilize, Shared deep Burial Encapsulation

## Slide 16: Disposal of Healthcare Waste Cont’d…
Non Sharp
Clinical Waste – from Patient care
Laboratory
Plastics
Disposable Syringes, IV Sets, Catheters ET Tubes
Steam Sterilize and Shared
Landfill
Non Plastics
Cotton, Gauze Dressing Contaminated With Blood, Purulent Exudate, Secretions and Excretions
Steam Sterilize and Shred or Incineration
Landfill

## Slide 17: Disposal of Healthcare Waste Cont’d…
Laboratory
Specimens
Anatomical Parts, Animal Carcasses
Blood, Body Fluids, Secretions and Excretions
Microbiology Lab. Waste
Steam Sterilize
Landfill
Steam Sterilization and Shred
Sewer or Landfill
Incineration/ Cremation
Ash to Landfill

## Slide 18: Summery