## Slide 1: Volume 2_Section 4 CHAPTER 3: IPC IN CLINICALLABORATORY SERVICES
Infection Prevention and Control in special setting

## Slide 2: Chapter contents
Overview
Laboratory-acquired infections
Common routes of Exposure that can result in Laboratory-acquired infections
Factors Contributing to Laboratory accidents
Laboratory Biosafety
Safe Work practices and Recommended infection prevention practices for laboratory workers
Infection prevention and control for specific laboratory procedures

## Slide 3: Learning Objective
By the end of this chapter, participants will be able to:
Describe Laboratory Acquired Infections
Identify Common Routes of Exposure to Laboratory-acquired infections
Describe Laboratory Bio-safety
Identify safe work practices and recommended infection prevention practices for laboratory workers in specific laboratory procedures

## Slide 4: 1. OVERVIEW (1/1)
The clinical laboratory is a unique area of the health care facility.
Error, accident, or carelessness in the handling of specimens and pathogens is the cause of most laboratory acquired infections.
Infections such as brucellosis, tuberculosis, typhoid, hepatitis, streptococcal infections, and others are known to have been acquired from the laboratory.

## Slide 5: 2. Laboratory-acquired Infections (1/1)
Laboratory acquired infection (LAI) is an infection obtained through laboratory or laboratory-related activities as a result of work with infectious biological agents.

## Slide 6: 3. Common Routes of Exposure That Can Result In LAI (1/1)
Inhalation.
Ingestion
Puncture Wounds
Contamination of Skin and Mucous Membranes
Infected Laboratory Animals

## Slide 7: 4. Factors Contributing To Laboratory Accidents (1/1)
Poor training.
Lack of concentration.
Carelessness and negligence.
Overwork and fatigue-emergency conditions.
Untidy and noisy working environment.

## Slide 8: 5. Laboratory Bio-safety (1/2)
This is a “containment” principles, technologies, practices implemented to prevent unintentional exposure to pathogens and toxins, or their accidental release.
The term “containment” is used in describing safe methods, facilities and equipment for managing infectious materials in the laboratory environment where they are being handled or maintained.

## Slide 9
Bio-safety level (BSL) Guidelines - is a combination of primary and secondary containment and safety guidelines designed for use in microbiology laboratories and bacteriology research units functioning at four levels (BSL-1 to BSL-4) of increasing risk:
Biological Safety Cabinets (BSCs) - these are devices that provide protection for the staff, the agent being processed, and the environment.
Laboratory Bio-safety… (2/2)

## Slide 10: 6. Safe Work Practices and Recommended IP Practices For Laboratory Workers (1/5)
Most hospital or clinic laboratories are defined as BSL-1 or BSL-2 units.
Prevention of occupationally-acquired infections in these laboratories consists of staff conscientiously using the basic practices prescribed for all healthcare workers namely Hand hygiene (hand washing or use of an antiseptic hand rub)

## Slide 11: Requirements For Safe Laboratory Practice (2/5)
Appropriate laboratory design (superstructure, furniture and space).
Adequate light, water, sewage, ventilation and electrical facilities.
Waste disposal facilities.
Appropriate storage of facilities.
Use of safety devices and bio-safety cabinets.
Restricted access to laboratories

## Slide 12: General Laboratory Safety Procedures (3/5)
Wear new examination gloves when handling blood, body fluids and/or specimens containing pathogenic microorganisms.
No eating, drinking or smoking is permitted in the laboratory.
Food should not be stored in refrigerators used for clinical or research specimens.
No mouth pipetting is permitted;

## Slide 13: General Laboratory Safety … (4/5)
Do not open centrifuges while still in motion.
Always cover the end of blood collection tubes with a cloth or paper towel or point them away from anyone’s face when opening.
Decontaminate working surfaces daily or when contaminated (e.g. after spills, with a 0.5% Chlorine solution).

## Slide 14: General Laboratory Safety …(5/5)
Wear protective face shields or masks and goggles
Wear heavy-duty or utility gloves when cleaning laboratory glassware.
Use puncture-resistant and leak proof containers for sharps
Place infectious waste materials in plastic bags or containers
Immunization against highly infectious agents such as HBV

## Slide 15: 7. IPC For Specific Laboratory Procedures (1/2)
Drawing blood from veins of patients (phlebotomy) is often performed by laboratory staff.
Safe Handling of Specimens
Specimen containers and labels
Transporting specimens within the health care facility
Receipt of specimens

## Slide 16: IPC For Specific …(2/2)
Safe Laboratory Bench Workspace
Use of pipettes and pipetting aids
Separation of serum
Use of centrifuges

## Slide 17: Summary (1/1)
The clinical laboratory is a unique area of the health care facility where Error, accident, or carelessness in the handling of specimens and pathogens is the cause of most laboratory acquired infections.
Common routes of Exposure to LAI includes: Inhalation, Ingestion, Puncture Wounds, Contamination of Skin and Mucous Membranes, Infected Laboratory Animals
Identifying and improving factors contributing laboratory accidents
Implementation of General laboratory Safety and Procedures.